## Slide 1: LPG GAS AUTOMATION USING IoT
UNDER THE GUIDANCE OF
Mr.J.KALIDASS, M.E.,
ASSISTANT PROFESSOR/IT,
GOVERNMENT COLLEGE OF TECHNOLOGY.
BY
NANCY A(1418127).
NISHA S(1418132).
SIVASANKARI P(1418144).
NAGALAKSHMI L(1418l05)

## Slide 2: OBJECTIVE
To develop a portable, user friendly Android application which controls on/off of gas cylinder.
It also performs automatic gas booking, gas leakage detection and also monitoring the gas level in the cylinder.
This is done with the help of Arduino board through IoT.

## Slide 3: EXISTING SYSTEM
A. IVRS
B. SMS
C. ONLINE BOOKING
IVRS was introduced due to the user’s complaints regarding to the landline phones of the distributer’s .
Landline phones are not giving response to the users call or the call line is busy and also in the IVRS user required to follow the instructions according to their format which is very confusing process.

## Slide 4: CONTINUED..
ONLINE BOOKING :
little time consuming process
It required some knowledge about the messaging
Mostly users are not able to guess the level of LPG gas in cylinder
SMS :
It required std code and distributer mobile no. SMS < IOC > to the same mobile number where booking is made .

## Slide 5: PROPOSED SYSTEM
A portable Android application which contains the following features:
User Authentication
Controlling on/off of gas cylinder
Auto gas booking.
Gas leakage detection.
Gas level monitoring.

## Slide 6: LITERATURE SURVEY
TITLE | AUTHOR | YEAR | TECHNIQUE | ADVANTAGE | DISADVANTAGE
Embedded control system for LPG leakage detection | Sunithaa J Sushmitha D | April,2012 | Interactive Voice Response | Response for the user is given properly. | Difficult to upgrade
Security Alert System using GSM | Ranjitha S Swapna T | October,2012 | GSM | SMS alert is sent. | Authentication problem.
LPG Booking, Leakage Detection . | Gawai NS | April,2015 | Sensor Monitoring | Exhaust fan and Activation of Alarm. | Equipments are costly.

## Slide 7: PROBLEM DEFINITION
The proposed system rectifies authentication problem by the process checking user account permission for access.
As the system embedded with arudino board so the upgrade is done easily.
With the help of valve the automatic ON/OFF of the cylinder is performed.

## Slide 8: MODULES DESCRIPTION
User Authentication.
Controlling on/off of gas cylinder.
Auto gas booking.
Gas leakage detection.
Gas level monitoring.

## Slide 9: User Authentication
The process of an administrator granting rights and the process of checking user account permissions for access to resources are both referred to as authorization.
The privileges and preferences granted for the authorized account depend on the user’s permissions, which are either stored locally or on the authentication server.

## Slide 10: Controlling on/off of gas Cylinder
Aims at designing a system that detects gas is ON and alerts the subscriber through an alarm.
Sends alert SMS on user Android Mobile App and turning off the gas supply valve as a primary safety measure.
Will be able to control the regulator using an Android app through which he can detect the status and switch off the regulator if necessary using a Wi-Fi module.

## Slide 11: Auto gas Booking
In auto gas booking we continuously measure the amount of gas which is present in the cylinder.
When gas level goes below the set level then message will be send to the gas agency through GSM and confirmation message received by the user from gas agency.
So user get cylinder within time.

## Slide 12: Gas leakage detection:
The highly useful home application – Gas Leakage Detector using Arduino and GSM Module with SMS Alert and Sound Alarm.
LPG Sensor Project using Arduino and MQ2 sensor, which senses lpg leak and produces sound alarm

## Slide 13: Gas level monitoring
The LPG in the cylinder using load sensor and if the level is below the threshold limit the system inform them by SMS and also by the display with Android mobile application.
So that the user have an idea about the max time the LPG lasts.
An automatically booking of the cylinder using a GSM module is also used in this proposed system.

## Slide 14: BLOCK DIAGRAM
ARDUINO
GAS
SENSOR
GSM MODULE
POWER SUPPLY
LOAD CELL
DRIVER CIRCUIT
BUZZER
16 X 2 LCD
MOTOR

## Slide 15: ARUDINO

## Slide 16: CONCLUSION
This system detects the leakage of the LPG and alerts the consumer about the leak by SMS.
As an emergency measure the system will turn off the power supply, while activating the alarm.
The cost involved in developing the system is significantly low.

## Slide 17: REFERENCES
[1] Sunithaa.J, Sushmitha.D, “Embedded control system for LPG leakage detection and prevention” International Conference on Computing and Control Engineering (ICCCE 2012), 12 & 13 April, 2012.
[2] S. Ranjitha, T .Swapna, “A Security Alert System Using GSM for Gas Leakage”, International Journal of VLSI and Embedded System (IJVES) Vol. 3, Issue 4, September –October 2012
[3]Potdukhe, N.S.Gawai, “Automatic LPG Booking, Leakage Detection and real Time Gas Measurement Monitoring System”, International Journal of Engineering Research and Technology (IJERT) Vol. 2, Issue 4, April 2013

## Slide 18
Thank you